УДК 004.942:621.6:622.691

Чисельне моделювання несталих режимів транспорту природного газу

по багатонитковому магістральному газопроводу / Буданцева Ю. В.,

Гусарова І.Г., Тевяшев А.Д. // Вісник Харк. нац. ун-ту., – 2008. – № 833. Сер.

«Математичне моделювання. Інформаційні технології. Автоматизовані

системи управління», вип.10. – С. 59-72: мал. 5. - табл. 1. – Бібліогр.: 7 назв.

Дана робота присвячена питанням математичного моделювання

нестаціонарних неізотермічних режимів транспорту природного газу (ННРТПГ)

по багатонитковому магістральному газопроводу (БМГ), який складається з

ділянок трубопроводу та компресорних станцій. Пропонується метод

розв'язання рівнянь математичної моделі, побудованої з урахуванням структури

БМГ, який дозволяє розраховувати та проводити аналіз ННРТПГ по БМГ. Данні

розрахунки можуть бути використанні при прогнозуванні ННРТПГ, при

оперативному керуванні режимами, а також у випадках прийняття рішень в

аварійних ситуаціях.

UDC 004.942:621.6:622.691

Numerical simulation of unsteady modes of transport of natural gas on the

multistrand main gas pipeline / Budantseva Yu. V., Gusarova I. G., Tevyashev

A. D. // Bulletin of V. Karazin Kharkiv National University, – 2008. – № 833.

Series «Mathematical Modelling. Information Technology. Automated Control

Systems», Issue 10. – P. 59-72: Pic. 5. – Tabl.1. – Ref.: 7 title (In Russian)

This work is devoted to the questions of numerical simulation of the unstationary

unisothermal modes of transport of natural gas (UUMTNG) on the multistrand main

gas pipeline (MMGP). MMGP consists of pipeline sections and compressor stations.

The method of solving equations of mathematical model, built on the basis of structure

of MMGP, allowing to calculate and analyze the UUMTNG on the MMG is offered.

These calculations can be used for prognostication of UUMTNG, at an operative

management the modes, and also in the case of decision-making in the emergency

situation.

Keywords: multistrand main gas pipeline, mathematical model, unstationary

unisothermal modes of transport of natural gas, method of decision, finite-difference

scheme, Newton's method