УДК 621.039:004.05

(n,m)-версійні системи: таксономія, моделі та технології / Сіора О.А.,

Скляр В.В., Харченко В.С. // Вісник Харк. нац. ун-ту., - 2008. - № 833. Сер.

“Математичне моделювання. Информаційні технології. Автоматизовані

системи управління”, вип. 10. – С.231-246: мал. 4. – табл. 2. –

Бібліогр.: 32 назв.

Уточнено базові поняття диверсності як ключового принципу зменшення

імовірності відмови за загальною причиною комп’ютерних систем.

Запропонована таксономічна схема, що включає взаємопов’язані поняття версії,

багатоверсійності, версійної надмірності, багатоверсійної (n,m-версійної)

системи, технології та проекту. Проаналізовано відомі класифікації видів

версійної надмірності та запропоновано використовувати тримірну матрицю

(“куб багатоверсійності”) з координатами “стадії та процеси життєвого циклу -

рівень представлення – багатоверсійні проектні рішення”. Узагальнено моделі

(n,m)-версійних систем. Визначено показник ефективності використання

версійної надмірності як питомий приріст надійності та безпеки на одиницю

витрат.

UDC 621.039:004.05

(n,m)-Version Systems: Тaxonomy, Models and Technologies / Siora A.A.,

Sklyar V.V., Kharchenko V.S. // Bulletin of V. Karazin Kharkiv National

University, – 2008. – № 833. Series «Mathematical Modelling. Information

Technology. Automated Control Systems», Issue 10. – P. 231-246: Pic. 4. –

Tabl. 2. - Ref.: 32 titles (In Russian)

Basic concepts of diversity as key approach to decreasing probability of common

cause failure of computer-based systems are specified. The taxonomic scheme

including interconnected concepts of a version, multiversity, version redundancy,

multi-version (n,m-version) system, multi-version technology and project is desсribed.

Known classifications of version redundancy kinds are analyzed and it’s suggested to

use three-space matrix (“cube of multiversity”) with coordinates “lifecycle stages and

processes – level of presentation – multi-version project decisions”. Models of n,mversion

systems are generalized. It’s specified an indicator of cost-effectiveness of

using version redundancy as specific increasing of dependability.

Keywords: common cause failure, taxonomy, multiversity, version redundancy,

multi-version project, lifecycle stages, dependability.