УДК 532.516

Моделювання нестаціонарних турбулентних течій при обтіканні рухливих тіл складної геометрії на основі рівнянь Нав’є-Стокса / Дзензерський В. О., Приходько О. А., Редчиць Д. О., Хачапурідзе М. М. // Вісник Харк. нац. ун-ту., – 2009. – № 847. Сер. «Математичне моделювання. Інформаційні технології. Автоматизовані системи управління», вип. 11. – С. 150-166: мал. 20. – Табл. 0. – Бібліогр.: 50 назв.

Для чисельного моделювання нестаціонарних турбулентних відривних нестисливих течій застосовуються осереднені за Рейнольдсом рівняння Нав’є-Стокса. При моделюванні турбулентності використовуються однопараметричні диференціальні моделі турбулентності. Виконано порівняння результатів розрахунків обтікання нерухомого профілю та профілю, що коливається. Представлено результати розрахунків роторів Дар’є та Савоніуса з різною кількістю й геометричними характеристиками лопатей. Виконано аналіз поля течії навколо роторів. Виділено основні стадії формування вихрової структури. Встановлено вплив чисел Рейнольдса, коефіцієнтів швидкохідності й заповнення на енергетичні характеристики роторів Дар’є та Савоніуса.

UDC 532.516

Simulation of unsteady turbulent flows around moving complex geometry bodies on the base of Navier-Stokes equations/ Dzenzerskiy V. A., Prykhodko O. A., Redchyts` D. O., Khachapuridze M. M. // Bulletin of V. Karazin Kharkiv National University, – 2008. – № 847. Series «Mathematical Modelling. Information Technology. Automated Control Systems», Issue 11. – P. 150-166: Pic. 20. – Tabl. 0. – Ref.: 50 titles (In Russian)

The Reynolds averaged Navier-Stokes equation were applied to a numerical simulation of unsteady turbulent separated incompressible flows. The one-equation turbulence models were used. Comparison of results of calculations flow near fixed and oscillating airfoil was carried out. The results of calculation of Darrieus and Savonius rotors with different quantity and geometrical performances of blades are submitted. The analysis of flow field near rotors was carried out. The main stages of development of vortex were allocated. The influence of Reynolds numbers, tip-speed-ratios and solidity on power characteristics of Darrieus and Savonius rotors was found.

Keywords: Navier-Stokes equation, Reynolds averaged, numerical simulation, one-equation turbulence model, Darrieus and Savonius rotors, power characteristics.