УДК 533.6.013.42

Моделювання навантаження парашутів з урахуванням зміни форми та фільтраційної здатності куполу / Морозов В. І., Пономарьов А.Т.// Вісник Харк. нац. ун-ту., – 2008. – № 809. Сер. «Математичне моделювання. Інформаційні технології. Автоматизовані системи управління», вип. 9. – С. 148-161: мал. 9.– Бібліогр.: 28 назв.

Здійснено дослідження щодо визначення розподілених та інтегральних аеродинамічних характеристик розкритих парашутів із різноманітними формами куполів за різними кутами атаки на малих швидкостях. Досліджено вплив зміни форми купола та проникної здатності тканини. Обчислення виконані за допомогою АІС «Купол», що базується на розрахунковій дискретній та аеродинамічній вихровій схемах, які побудовані відповідно обчислювальних методах концентрованих мас та вихрових рамок. Остання використовує модель ідеальної рідини, що не стискається, та ігнорує вплив строп на відрив вихорів.

UDC 533.6.013.42

The modeling-of load a parachute, taking into account the form and permeability of the dome / Morozov V. I., Ponomaryov A.T. // Bulletin of V. Karazin Kharkiv National University, – 2008. – № 809. Series «Mathematical Modelling. Information Technology. Automated Control Systems», Issue 9. – P. 148-161: Pic. 9.–Ref.: 28 titles (In Russian)

Results of the researches of the distributed and integrated aerodynamic characteristics of the filled parachutes with domes various forms (round, square, crosswise) are resulted at different angles of attack on small subsonic speeds. Influence on them of change of the form of a dome, and also permeability of its fabric is thus considered. Calculations are executed by means of the automated system "Dome" which base are settlement discrete elastic and aerodynamic vortical schemes, on the basis of numerical methods accordingly localised masses (МСМ) and vortical frameworks (МВР) with use of model of an ideal incompressible liquid (places of separation of a stream are set, influence of strips on parachute flow past is not considered).

Keywords: aerodynamic characteristics, parachute, dome, permeability, discrete elastic system, aerodynamic vortical scheme, МСМ, МВР, incompressible liquid